APPENDIX  7.1

National Ambient Air Quality Standards

| Pollutants | Time Weighted Average | Concentration in ambient air | Method of measurement |
| --- | --- | --- | --- |
|  |  | Industrial Area | Residential Rural & other areas | Sensitive Area |  |
| Sulphur Dioxide(SO2) | Annual Average* | 80 g/m3 | 60 g/m3 | 15 g/m3 | - Improved West and Geake Method - Ultraviolet Fluorescence |
|  | 24 hours** | 120 g/m3 | 80 g/m3 | 30 g/m3 |  |
| Oxides of Nitrogen as NO2 | Annual* | 80 g/m3 | 60 g/m3 | 15 g/m3 | - Jacob & Hochheiser Modified (Na-Arsenite) Method - Gas Phase Chemiluminescence |
|  | 24 hours** | 120 g/m3 | 80 g/m3 | 30 g/m3 |  |
| Suspended Particulate Matter (SPM) | Annual* | 350 g/m3 | 140 g/m3 | 70 g/m3 | High Volume Sampling, (Average flow rate not less than 1.1 m3/minute) |
|  | 24 hours** | 500 g/m3 | 200 g/m3 | 100 g/m3 |  |
| Respirable Particulate Matter (PM10) , size less than 10 m) | Annual* | 120 g/m3 | 60 g/m3 | 50 g/m3 | Respirable particulate matter sampler |
|  | 24 hours** | 150 g/m3 | 100 g/m3 | 75 g/m3 |  |
| Lead (Pb) | Annual* | 1.0 g/m3 | 0.75 g/m3 | 0.50 g/m3 | ASS Method after sampling using EPM 2000 or equivalent Filter paper |
|  | 24 hours** | 1.5 g/m3 | 1.00 g/m3 | 0.75 g/m3 |  |
| Carbon Monoxide (CO) | Annual* | 5.0 mg/m3 | 2.0 mg/m3 | 1.0 mg/m3 | Non dispersive infra red Spectroscopy |
|  | 24 hours** | 10.0 mg/m3 | 4.0 mg/m3 | 2.0 mg/m3 |  |
| Ammonia | Annual* | 100 g/m3 | 100 g/m3 | 100 g/m3 | -- |
|  | 24 hours** | 400 g/m3 | 400 g/m3 | 400 g/m3 |  |

*	Annual Arithmetic mean of minimum 104 measurements in a year taken twice a week 24 hourly at uniform interval.

** 24 hourly/ 8 hourly values should be met 98% of the time in a year. However, 2% of the time, it may exceed but on two consecutive days.

NOTE:

1.	National Ambient Air Standard: The levels of air quality with an adequate margin of safety, to protect the public health, vegetation and property.

2.	Whenever and wherever two consecutive values exceeds the limit specified above for the respective category, it would be considered adequate reason to institute regular/continuous monitoring and further investigations.